## Slide 1: ECL5/CATANA: Stability prediction at design and part speed
Ewan Gunn
Turbostream Ltd
26 March 2025

## Slide 2: Overview
Introduction and approach
Steady flow field at design speed (100%) and part speed (80%)
Design speed: Spike-type rotating stall
Part speed: Onset of unsteady flow
Conclusions

## Slide 3: Introduction and Approach

## Slide 4: Predicting stability limits in transonic fans
Transonic fan stability at low mass flow rates can be limited by different mechanisms, depending on the rotational speed
This typically divides the operating map into two or more regimes: Design speed: rotating stall Part speed: often vibration before stall: flutter, Non-Synchronous Vibration (NSV)
We aim to demonstrate an industrial framework to predict these limits with URANS simulations, within design timescales (hours or days)
Brandstetter, C., 2020, “Project CATANA Overview”
Schematic fan operating map with stability limits
Brandstetter, C., Fiquet, A., Schneider, A. P., Paoletti, B., and Ottavy, X. "Experiments on Tuned UHBR Open-Test-Case Fan ECL5/CATANA: Stability Limit." J. Eng. Gas Turbines Power. 2024; 146(5): 051011
ECL5/CATANA measured fan operating map with mode 2 vibration

## Slide 5: Approach: targeted simulations at 80% and 100% speed
Standard, un-tuned industrial transonic fan setup, as if carrying out a blind prediction
Rigid blade simulations that can predict rotating stall and purely aerodynamic unsteady flow (not flow-structure interaction)
100% speed: CFD predicts sudden spike-type rotating stall, consistent with the test Pre-stall flow field is steady: no precursors
80% speed: CFD predicts high-amplitude unsteady flow in the rotor at low mass flow rates, before reaching stall Conditions correspond to those where NSV is observed in the test
Brandstetter, C., Fiquet, A., Schneider, A. P., Paoletti, B., and Ottavy, X. "Experiments on Tuned UHBR Open-Test-Case Fan ECL5/CATANA: Stability Limit." J. Eng. Gas Turbines Power. 2024; 146(5): 051011
ECL5/CATANA measured fan operating map with mode 2 vibration

## Slide 6: Standard industrial RANS/URANS simulation setup
Simple extended inlet
Variable-area choked nozzle set to ambient back pressure
Mixing plane interface for steady simulations Sliding plane interface for unsteady simulations
Rotor
OGV
Turbostream 4: GPU-accelerated flow solver
Typical industrial multiblock structured fan grid: 3.1E6 cells per rotor passage, 0.94E6 cells per OGV passage Full-annulus total 80E6 cells
URANS: Full-annulus unsteady simulations with sliding plane interface using Jameson’s Dual Time Stepping (DTS) 1600 timesteps per rotor revolution; 2 hours per revolution on 8 NVIDIA H100 GPUs
Spalart-Allmaras model with velocity helicity, using adaptive wall functions SA-noft2-Helicity, https://turbmodels.larc.nasa.gov/spalart.html#helicity
Effect of shaft speed on rotor untwist and tip clearance included

## Slide 7: Steady Flow Field

## Slide 8: ECL5/CATANA steady performance map
EXP: Schneider, A. P., Fiquet, A., Paoletti, B., Ottavy, X., and Brandstetter, C., "Experiments on Tuned UHBR Open-Test-Case Fan ECL5/CATANA: Performance and Aerodynamics." J. Turbomach. 2024; 146(8): 081001
100% speed: Rotating stall observed in EXP Stability limit captured in steady and unsteady CFD
80% speed: Performance measurement EXP boundary at blade vibration limit Stable flow range overpredicted by steady CFD
Unsteady CFD can predict the onset of unsteady flow and improve accuracy of stability limit prediction
Supersonic relative inlet flow
EXP limit: rotating stall
Subsonic relative inlet flow
EXP limit: vibration
55%
70%
80%
100%
90%
105%
95%

## Slide 9: Steady CFD, 100%: blockage from shock-induced separation and endwall
AR = 0.655 Last stable point
AR = 0.675 Peak pressure ratio
AR = 0.825 Rotor peak efficiency
Rotor suction surface flow field
Contours of static pressure, limiting streamlines and shaded green isosurface of Vx = 0
Onset of TE separation
Shock-induced separation downstream of LE
Shock-induced separation begins to merge with casing BL into corner separation

## Slide 10: Steady CFD, 80%: onset of subsonic LE separation
AR = 0.575 Positive slope on characteristic
AR = 0.600 Peak pressure ratio
AR = 0.750 Rotor peak efficiency
Rotor suction surface flow field
Contours of static pressure, limiting streamlines and shaded green isosurface of Vx = 0
Subsonic inlet flow, but incidence leads to low-pressure spike at LE on suction surface
Full-span subsonic LE separation created as incidence is increased further

## Slide 11: Design Speed: Spike-Type Rotating Stall

## Slide 12: Stall simulation approach at 100% speed
First unsteady OP AR = 0.660 Stable
Second unsteady OP AR = 0.655 Stable
Trace from third unsteady OP AR = 0.650 Unstable
Steady
Stable unsteady OP (time average over last rev)
Instantaneous trace from unsteady OP
Approach follows Kim et al, 2019, Stall Inception in Low Pressure Ratio Fans, J. Turbomach., 141(7):
Start unsteady simulations from the second-last single-passage steady solution
Create a full-annulus version of the computational grid
Mis-stagger one rotor blade by 0.4° to provide a stall nucleation point, mimicking real-life asymmetries
Converge the unsteady simulation at the first nozzle setting, then incrementally close the exit nozzle
At each operating point, examine pressure traces and the rotor flow field for any signs of instability

## Slide 13: Classic spike stall observed in casing static pressure traces
Small perturbations from passing of mis-staggered blade
Rapid growth of spike stall cell
Fully developed rotating stall cell traveling circumferentially at ~68% of rotor shaft speed
Static pressure traces taken from unsteady pressure probes applied in the absolute reference frame in the CFD on the rotor casing at 10% of axial chord upstream of the rotor LE.
Before t = 0: stable flow in the rotor. Regular blade passing signal with small perturbations from the mis-staggered rotor blade
t = 0: Nozzle closed by one increment
After t = 0: sharp disturbance at t = 2 showing spike stall inception followed by propagation and growth
AR = 0.655
AR = 0.650
Static pressure fluctuation/circumferential coordinate: θ
0°
180°
Regular rotor blade passing signal at one circumferential position

## Slide 14: Time history of operating point from stall simulation
Overall and rotor mass flow rates
Overall pressure ratio
Rotor pressure ratio
OGV pressure ratio
AR = 0.660
AR = 0.655
AR = 0.650
Time axis is set to zero at the moment the nozzle is closed to AR = 0.650
Flow at AR = 0.660 is initialised from the single-passage solution and run unsteady for 4 revolutions
Nozzle closed to AR = 0.655 at t = -14 and the mass flow rate and pressure ratio adjust to the new operating point. Traces and flow field (shown on following slides) indicate flow is stable at this operating point
Nozzle closed to AR = 0.650 at t = 0. At this point the pressure ratio and mass flow rate drop more rapidly.

## Slide 15: Last stable operating point
AR = 0.655 t = 0.00 revs

## Slide 16: Growth of shock-induced separation
AR = 0.650 t = 2.00 revs

## Slide 17: Growth of shock-induced separation
AR = 0.650 t = 2.25 revs

## Slide 18: Growth of shock-induced separation
AR = 0.650 t = 2.50 revs

## Slide 19: LE separation, increase in incidence in neighbouring passage
AR = 0.650 t = 2.75 revs

## Slide 20: Stall cell propagates circumferentially
AR = 0.650 t = 3.25 revs

## Slide 21: Continued growth and propagation of stall cell
AR = 0.650 t = 3.50 revs

## Slide 22: Continued growth and propagation of stall cell
AR = 0.650 t = 3.75 revs

## Slide 23: Continued growth and propagation of stall cell
AR = 0.650 t = 4.00 revs

## Slide 24: Fully developed part-span rotating stall
AR = 0.650 t = 5.00 revs

## Slide 25: Fully developed part-span rotating stall
AR = 0.650 t = 6.00 revs

## Slide 26: Fully developed part-span rotating stall
AR = 0.650 t = 7.00 revs

## Slide 27: Blade-to-blade flow field: combination of blade and endwall blockage
Contours of axial velocity and radial vorticity on blade-to-blade surface at 97.50% span AR = 0.655
Mis-staggered blade
x
rθ

## Slide 28: Blade-to-blade flow field (static view)
Contours of axial velocity and radial vorticity on blade-to-blade surface at 99.75% span AR = 0.655
x
rθ

## Slide 29: Blade-to-blade flow field (detail view)
Axial velocity 97.5% span
Radial vorticity 97.5% span
Axial velocity 99.75% span
Radial vorticity 99.75% span
Low momentum/reversed flow in middle of passage originates from thickened casing boundary layer and indicates high blockage
Shock-induced separation on blade
Shock-induced separation on blade
Interface line between oncoming high-momentum flow and low-momentum/reversed flow
Area of low-momentum/reversed flow almost covers full passage, except for small area near pressure surface LE
Interface line between oncoming high-momentum flow and low-momentum/reversed flow almost covers full passage, but does not spill ahead of LE
Detail views at t = -1 with stable flow field highlight key flow features

## Slide 30: Blade-to-blade flow field: combination of blade and endwall blockage
Contours of axial velocity and radial vorticity on blade-to-blade surface at 97.50% span Exit nozzle closed from AR = 0.655 to AR = 0.650 at t = 0
x
rθ

## Slide 31: Blade-to-blade flow field (animations)
Contours of axial velocity and radial vorticity on blade-to-blade surface at 99.75% span Exit nozzle closed from AR = 0.655 to AR = 0.650 at t = 0
x
rθ

## Slide 32: Part Speed: Onset of Unsteady Flow

## Slide 33: Experimental observations at 80% speed: NSV at low flow rates
Brandstetter, C., Fiquet, A., Schneider, A. P., Paoletti, B., and Ottavy, X. "Experiments on Tuned UHBR Open-Test-Case Fan ECL5/CATANA: Stability Limit." J. Eng. Gas Turbines Power. 2024; 146(5): 051011
Low/negligible vibration amplitude observed above 25 kg/s. As mass flow decreases, the vibration amplitude increases rapidly to the limit at just over 23.5 kg/s

## Slide 34: Experimental observations and analysis at 80% speed: NSV at low flow rates
Brandstetter, C., Fiquet, A., Schneider, A. P., Paoletti, B., and Ottavy, X. "Experiments on Tuned UHBR Open-Test-Case Fan ECL5/CATANA: Stability Limit." J. Eng. Gas Turbines Power. 2024; 146(5): 051011
Measured fan operating map with mode 2 vibration
Strain gauge and tip timing modal amplitude measurements Amplitude increases rapidly below 25 kg/s
Absolute frame spectral analysis Dominant frequencies are below blade passing frequency, in range from ~5-10Ωr

## Slide 35: Spot-check unsteady simulations at 80% speed
EXP: Schneider, A. P., Fiquet, A., Paoletti, B., Ottavy, X., and Brandstetter, C., "Experiments on Tuned UHBR Open-Test-Case Fan ECL5/CATANA: Performance and Aerodynamics." J. Turbomach. 2024; 146(8): 081001
55%
70%
80%
100%
Four operating points selected
Four unsteady operating points selected at 80% speed
Each OP is run for a period of 4 rotor revolutions. Unsteady casing static pressure is extracted at 10% chord upstream of the rotor LE
Simulations run with rigid blades: aerodynamic unsteady flow is predicted, but not vibration or lock-in
AR 0.750
AR 0.600
AR 0.575
AR 0.565

## Slide 36: Unsteady simulations at 80% speed
AR 0.750 ~30.5 kg/s
AR 0.600 ~24.9 kg/s
AR 0.575
~24.0 kg/s
AR 0.565 ~23.5 kg/s
Spectra of absolute frame casing unsteady static pressure signals plotted at 10% chord upstream of rotor LE
Away from the stability limit, the spectra are dominated by the BPF and its harmonics, with negligible amplitude at other frequencies
Approaching the stability limit, amplitude increases around f = 9Ω and its harmonics
BPF

## Slide 37: Onset of unsteady flow at low mass flow rates
Brandstetter, C., Fiquet, A., Schneider, A. P., Paoletti, B., and Ottavy, X. "Experiments on Tuned UHBR Open-Test-Case Fan ECL5/CATANA: Stability Limit." J. Eng. Gas Turbines Power. 2024; 146(5): 051011
CFD captures the onset of unsteady flow within the frequency range identified in the test, but with a simpler spectrum
Simulation is for a fixed-blade, axisymmetric rotor. Measurements show that the unsteady flow excites blade motion, altering the relative-frame frequency spectrum
EXP
CFD

## Slide 38: Pattern of separated flow with increasing blockage at low flow rates
AR = 0.600 (~24.9 kg/s) Peak pressure ratio
AR = 0.565 (~23.5 kg/s) Limit of EXP range

## Slide 39: Unsteady blockage distribution in relative frame
x
rθ
AR = 0.600 (~24.9 kg/s) Peak pressure ratio
AR = 0.565 (~23.5 kg/s) Limit of EXP range
Contours of axial velocity on blade-to-blade surface at 97.50% span

## Slide 40: Unsteady blockage distribution in relative frame
x
rθ
AR = 0.600 (~24.9 kg/s) Peak pressure ratio
AR = 0.565 (~23.5 kg/s) Limit of EXP range
Contours of radial vorticity on blade-to-blade surface at 97.50% span

## Slide 41: Conclusions

## Slide 42: Conclusions
URANS simulations offer a way to predict transonic fan stability at both design and part speed
Single-passage steady simulations give useful insight into the flow field and blockage mechanisms, but they do not show:
  The exact route into rotating stall at high speed
  The onset of unsteady flow at low speed
  The response to installation geometry and/or inlet distortion – not covered here, but relevant for real engine fan applications
The results suggest that part-speed, pre-stall simulations with fixed axisymmetric blade geometry can highlight conditions where unsteady flow would be expected
Extensions to include realistic asymmetry and blade motion could increase the accuracy further and allow direct prediction of the vibration
The limiting mechanisms observed in ECL5/CATANA are both found with a single simulation setup with no tuning, so they could be carried out blind on new fan designs within design timescales